FLIR Systems, Inc.

D-Series Camera

Architect & Engineering Specifications

This document is controlled to FLIR Technology Level 1.  The information contained in this document pertains to a dual-use product controlled for export by the Export Administration Regulations (EAR).   FLIR trade secrets contained herein are subject to disclosure restrictions as a matter of law. Diversion contrary to US law is prohibited.  US Department of Commerce authorization is not required prior to export or transfer to foreign persons or parties unless otherwise prohibited.

Document Number: 427-9029-00-13

Version: 100

Issue Date:  March 2011

NOT USED

PRODUCTS

Outdoor Multi-sensor Dome Camera System

Functional Description

The Outdoor Multi-sensor Dome Camera System shall consist of a Thermal Security Camera and a Daylight Color Camera mounted in a pan/tilt Dome Enclosure. The dome attaches by a curved mounting arm to an Electronics Enclosure.

The Outdoor Multi-Sensor Dome Camera System shall provide both IP network video and simultaneous analog composite video.

The Outdoor Multi-sensor Dome Camera System shall provide standard NTSC or PAL analog composite video outputs (factory configured) to allow it to function as a direct replacement for daylight camera and to connect directly to digital video recorders, encoders and monitoring equipment. The analog video signals shall be available via BNC video output connectors.

The Outdoor Multi-sensor Dome Camera System shall be furnished in an IP-56 -rated outdoor enclosure assembly.  The assembly includes a Dome Enclosure with cameras, a curved mounting arm, and an Electronics Enclosure.  All cable connections shall be made inside of the Electronics Enclosure.  The Electronics Enclosure shall be provided with liquid-tight sealed cable gland fittings for the video, Ethernet, serial and power cables.

The Outdoor Multi-sensor Dome Camera System shall include grounding and surge protection. A separate Earth ground connection shall be made inside the Electronics Enclosure to a designated grounding lug.  The Earth ground conductor may be run as part of the power cable bundle.

The Outdoor Multi-sensor Dome Camera System shall allow configuration of serial communications parameters (such as device address, baud rate, and so on) by means of hardware DIP switches or by means of software configuration with a web browser. A single DIP switch shall be used to select if the camera is configured with hardware or software.

The Outdoor Multi-sensor Dome Camera System shall feature an IP network interface, built-in Ethernet port, built-in web browser interface / Nexus server for device set-up, configuration and control.

The Outdoor Multi-sensor Dome Camera System shall allow the IP Interface to be reset to factory configuration by means of a simple Ethernet loopback cable.

The Outdoor Multi-sensor Dome Camera System shall provide two independent IP network streams (channels) of user selectable MPEG-4, H.264 or M-JPEG digital.

From a computer or other device, the Outdoor Multi-sensor Dome Camera System shall support set-up, configuration and control as follows:

Support a standard web browser interface.

Provide a software utility such as FLIR Sensors Manager (FSM) which shall be included with each Thermal Security Camera.

Support for third-party systems using the Nexus Software Development Kit (SDK) and a Common Gateway Interface (CGI) Application Programming Interface (API).

Configuration settings shall include settings for the video CODEC, serial communications interface, cameras sensors settings, etc.

The Outdoor Multi-sensor Dome Camera System shall use the embedded Nexus server to provide plug and play integration with FSM to enable sophisticated sensor management capabilities such as geo-referenced mapping, video analytics, slew-on-alarm and radar slew-to cue.

The Outdoor Multi-sensor Dome Camera System shall provide an IP network interface that is based on open standards to insure compatibility with a wide range of third-party video players and Video Management Systems (VMSs), such as, but not limited to, Milestone, Genetec and ONSSI.

The Outdoor Multi-sensor Dome Camera System shall be ONVIF compliant.

The Outdoor Multi-sensor Dome Camera System shall provide a RS-232/422 serial interface port for set-up, configuration and control.

The Outdoor Multi-sensor Dome Camera System serial port shall support both Pelco D and Bosch protocols allowing set-up, configuration, and control from a wide variety of devices.

The Outdoor Multi-sensor Dome Camera System shall operate as a hybrid device by providing both analog video (NTSC or PAL) simultaneously with IP video.  This dual-mode operation will allow the camera to provide video to both analog and IP networks at one time.

The Thermal Security Camera shall not depend on any visible or invisible (infrared) illumination or image intensifier to “see” i.e. produce images.  The Thermal Security Camera shall be totally passive and not produce any energy or emit light in any bandwidth.  The Thermal Security Camera shall allow the user to clearly identify images in the total absence of light.

The Thermal Security Camera shall allow the user to see through smoke and light fog and to view the thermal patterns and contrast in the scene.

The Thermal Security Camera shall utilize a Vanadium Oxide (VOx) uncooled microbolometer responding in the LWIR (Long Wave Infrared) spectral range of 7.5 – 13.5 μm which is beyond what is visible to the human eye.

The Thermal Security Camera shall be based on Vanadium Oxide (VOx) microbolometer detector technology, and shall thus not be susceptible to permanent damage after imaging the sun.  This is in contrast to some systems based on amorphous silicon detector technology which can be permanently damaged when viewing the sun or even reflections of the sun.

The Thermal Security Camera shall not utilize shutters to prevent damage from the sun, but rather the Thermal Security Camera shall provide uninterrupted video which shall be required for security installations.

The Thermal Security Camera shall include a lens or window that is temperature controlled to prevent dew, frost and ice accumulation.

The Thermal Security Camera shall not utilize dynamic apertures to protect the image sensor because these mechanisms reduce sensitivity for an extended period of time, thus reducing the Thermal Security Camera performance which shall not be acceptable for security installations.

The Thermal Security Camera shall provide athermal optics that automatically adjust to ambient temperature changes, and therefore do not require re-adjustment and/or thermal refocusing.

The Thermal Security Camera shall not be susceptible to “image blooming” caused by bright lights as are image intensifiers and visible spectrum cameras.

The range of the Thermal Security Camera shall be defined at three levels consisting of:

Detection – In order to detect if an object is present or not, its critical dimension needs to be covered by 1.5 or more pixels.

Recognition – Recognizing an object is defined as seeing what type of object it is.  This means being able to determine if the object is a person, a car or a truck.  In order to recognize an object it needs to be subtended by at least 6 pixels across its critical dimension.

Identification – Identifying the object is defined as seeing if it is a man/woman or a man carrying a shovel verses a man carrying a rifle.  In order to identify an object it needs to be subtended by at least 12 pixels.

The Thermal Security Camera shall be factory configured with one of the following fixed anti-reflection coated Germanium lenses with the Field of View (FOV) and resolutions as indicated:

| Device | Lens | Resolution (pixels) | FOV |
| --- | --- | --- | --- |
| D-313 | 35 mm | 320 x 240 | 13° H x 10° V |
| D-324 | 19 mm | 320 x 240 | 24° H x 19° V |
| D-334 | 13 mm | 320 x 240 | 34° H x 28° V |
| D-348 | 9 mm | 320 x 240 | 48° H x 39° V |
| D-618 | 35 mm | 640 x 480 | 18° H x 14° V |
| D-625 | 25 mm | 640 x 480 | 25° H x 20° V |
| D-645 | 13 mm | 640 x 480 | 45° H x 37° V |

Table 1:	Field of View (FOV)

The approximate DRI (Detection, Recognition, and Identification) range for a vehicle and a human target with each of the lenses listed in Tables 2 & 3.

| Device | Lens | Detection | Recognition | Identification |
| --- | --- | --- | --- | --- |
| D-313 | 35 mm | 2,150 m | 560 m | 280 m |
| D-324 | 19 mm | 1,280 m | 330 m | 165 m |
| D-334 | 13 mm | 840 m | 215 m | 108 m |
| D-348 | 9 mm | 590 m | 150 m | 74 m |
| D-618 | 35 mm | 3000 m | 800 m | 400 m |
| D-625 | 25 mm | 2,150 m | 560 m | 280 m |
| D-645 | 13 mm | 1,430 m | 360 m | 180 m |

Table 2:	DRI range for Vehicle (2.3 m x 2.3 m critical dimension)

| Device | Lens | Detection | Recognition | Identification |
| --- | --- | --- | --- | --- |
| D-313 | 35 mm | 780 m | 190 m | 97 m |
| D-324 | 19 mm | 450 m | 112 m | 56 m |
| D-334 | 13 mm | 300 m | 74 m | 37 m |
| D-348 | 9 mm | 205 m | 52 m | 26 m |
| D-618 | 35 mm | 1140 m | 280 m | 142 m |
| D-625 | 25 mm | 780 m | 190 m | 97 m |
| D-645 | 13 mm | 500 m | 127 m | 63 m |

Table 3:	DRI range for Human Target (1.8 m x 0.5 m critical dimension)

The Noise Equivalent Temperature Difference (NETD) is the measure of the smallest object temperature that can be detected by the thermal image sensor relative to the system noise.  The measurement is usually quantified as an mK value.  This is the most common Figure of Merit of a thermal imaging system and a true measurement of the thermal camera’s sensitivity.  The Thermal Security Camera image sensor shall provide a NETD of <50mK at f/1.0 or lower.

The Thermal Security Camera shall include Auto Digital Detail Enhancement (Auto DDE) which is an advanced non-linear image processing algorithm.  The Auto DDE function is fully automatic and requires no input or adjustment from the user.  The Auto DDE shall enhance the image detail to match the total dynamic range of the original image allowing details to be visible to the user even in scenes with low or high thermal contrast.  Auto DDE will increase the probability of detection of low contrast images.

The Thermal Security Camera shall utilize Non-Uniformity Correction (NUC) which is a set of compensation factors for each pixel.  NUC shall enable the following features and benefits:

Eliminate the need for FPA (Focal Plane Array) temperature stabilization.

Allow for near instantaneous camera turn-on.

Reduced system complexity and power consumption.

Allow for a wider operating temperature range.

The Thermal Security Camera shall include Automatic Gain Control (AGC) circuitry to compensate for scene variations, improve image quality by avoiding saturation and distortion, and to balance signal levels prior to display to maximize image quality.

The Thermal Security Camera shall feature both White-Hot and Black-Hot operating modes.  In the White-Hot (default) mode warmer images will be displayed in white or lighter shades than cooler or background areas.  In the Black-Hot mode warmer objects will be displayed as black or dark gray compared to cooler objects.

The Color Daylight Camera shall be provided with a high resolution CCD imager with a 36x optical zoom and 12x digital zoom lens, automatic IR cut-filter.

The pan/tilt Dome Enclosure shall be a multi-sensor camera unit consisting of a thermal imaging camera with a fixed focal length lens and a daylight camera with a continuous zoom lens integrated onto a high performance pan/tilt drive and rated for outdoor installations.  The pan drive shall be capable of true 360° rotation.

The pan/tilt Dome Enclosure shall be high-performance and provide continuous  360° pan motion at a rate of  0.1° to 70°/second, and tilt motion of +20° to -90° at a rate of 0.1° to 70°/second.

An online site security planning tool shall be available to assist the user in selecting the correct cameras and designing a video surveillance system.  The tool shall utilize Google Earth maps saved as jpeg images to allow the user to place cameras on the site / buildings and simulate the actual field of view of any camera to visually see the difference between each camera / lens combination for detection, recognition and identification.  The tool shall be available at http://raven.flirops.com/.

Technical Specifications

The Outdoor Multi-sensor Dome Camera System shall meet the following minimum requirements:

| Camera Platform Type | Dome Multi-Sensor |
| --- | --- |
| Composite Video Output | NTSC or PAL |
| Independent Streaming IP Video Channels | 2 for each of two cameras (thermal and daylight) |
| Available IP Network Video Formats | Streaming MPEG-4, H.264, M-JPEG |
| Serial Control Interface | RS-232/422; Pelco D, Bosch protocol |
| Ethernet Interface | RJ-45 |
| User Control Interface | Via devices supporting Pelco-D, Bosch protocols or Ethernet control via FLIR Sensors Manager (FSM), the Nexus SDK, the Nexus CGI commands, ONVIF, Milestone, Genetec and ONSSI |
| Input Voltage | 24 VAC nominal (21-30 VAC) 24 VDC nominal (21-30 VDC) |
| Power Consumption | 24 VAC: 85 VA max including heater 24 VDC: 75 W max including heater |
| Inrush Current | DC 5 A with 50 msec rise of the DC source AC 12A, 8.3msec using 60HZ AC power line |
| Operating Temperature Range | -32°C to 55°C (25.6° F to 131° F) |
| Storage Temperature Range | -40°C to 85°C (-40° F to 185° F) |
| Lens Heater | Thermostatically Controlled |
| Enclosure Rating | IP-56 |
| Weight | ~23 lb (10.5 kg) - configuration dependent |
| Dimensions (L, W, H) | (L,W,H) 7.8” × 18.5” × 21.8” (198.7 mm × 471 mm × 555.6 mm) |

The Thermal Security Camera shall meet the following minimum requirements:

| Sensor Type | Long-life, Uncooled VOx Microbolometer |
| --- | --- |
| Spectral Response | 7.5 to 13.5μm |
| Thermal Sensitivity | <50mK f/1.0 |
| Pixel Pitch | 3xx: 25μm 6xx:17μm |

The Color Daylight Camera shall meet the following minimum requirements:

| Camera | Sony FCB-EX1010 |
| --- | --- |
| Sensor Type | 1/4” Exview HAD CCD |
| Lens Field Of View | 57.8° (h) to 1.7° (h) |
| Focal Length | 3.4 mm to 122.4 mm |
| Zoom | 36× Optical zoom, 12× E-zoom |
| F/# | 1.6 to 4.5 |
| Effective pixels | (NTSC) 380,000 |

The Pan/Tilt Mechanism shall meet the following minimum requirements:

| Pan Angle/Speed | Continuous 360°; 0.1° to 70°/sec |
| --- | --- |
| Tilt Angle/Speed | +20° to -90°; 0.1° to 70°/sec |
| Programmable Presets | 128 |

The Thermal Security Camera shall be a FLIR D-Series Camera.

# Text boxes

FLIR Systems, Inc.

Commercial Systems

70 Castilian Drive

Goleta, CA 93117

1-877-773-3547

http://www.cvs.flir.com/security/